## Slide 1: Development of a Resilience Model for the Analysis of Process Systems at the Early Design Stage
Freya Vesey1,2 , Joan Cordiner1
1The University of Sheffield
2Cavendish Nuclear

## Slide 2: Limitations of Traditional Safety Analysis
Severe hazards that can’t be completely protected against
Severe hazards, inadequately considered due to their low-frequency
Underestimated or completely unexpected hazards
Beyond Design Basis Events
[1] Azadeh, A., Salehi, V., Arvan, M. and Dolatkhah, M., 2014. Assessment of resilience engineering factors by fuzzy cognitive maps. Safety Science, [online] 68, pp.99-107.
[2] MacAskill, K., 2021. Resilience Engineered - Demystify resilience with this three-part film series. [online] The Resilience Shift
Matrix employed in risk analysis [4]
[3] Pitblado, R., Fisher, M. and Nelson, B., 2016. Dynamic Barrier Management. HAZARDS 26, [online] (161), pp.1-8.
[4] Bridges, B., 2014. More on the Use of Risk Matrices in PHAs/HAZOPs. [online] Process Improvement Institute.

## Slide 3: What is Resilience?
A Resilient System can withstand variation, absorb impact and recover
Very useful for considering beyond design basis events
Resilience investments must be highly effective and low cost
[1] Gilbert, S., 2010. Disaster Resilience. U.S. Department of Commerce National Institute of Standards and Technology, [online] 1117, pp.1-113.
[2] World Economic Forum. 2022. Resilience Consortium. [online]
Source: [2]

## Slide 4: A New Approach to Resilience
The presented model will differ from existing resilience models by:
Avoiding reliance on complex system modelling
Giving a single value for a systems, describing its resilience to a wide range of beyond design basis events
Giving an indication of the system properties of which resilience is a function of
[1] Yodo, N. and Wang, P., 2016. Engineering Resilience Quantification and System Design Implications. Journal of Mechanical Design, [online] 138(11), pp.1-13.

## Slide 5: Model Framework
Resilient Design – how resilient the system is
Potential Impact – the severity of potential consequences to impact
Vulnerability – a systems susceptibility to severe hazards

## Slide 6: Resilient Design
Dimensions
Indicators
Metrics

## Slide 7: Potential Impact
Potential for Economic Impact:
Potential for economic impact = CC + R
CC – Capital Cost
R – Yearly Revenue
Potential Impact =
Potential for Human Health and Environmental Impact:
Potential for Impact to Human Health and the Environment = CHP ( H + E )
CHP – Chemical Hazard Potential
H – Human Health Impact Rating
E – Environmental Impact Rating
(CC + R) + CHP ( H + E )

## Slide 8: Vulnerability
Cascade failure → uncontrolled consequences to an initial impact
CHP is modified to describe hazards due to fire and explosion only
Vulnerability =
CHPi + CHPp
CHPi – CHP due to ignition
CHPp – CHP due to excess pressure
[1] Darbra, R., Palacios, A. and Casal, J., 2010. Domino effect in chemical accidents: Main features and accident sequences. Journal of Hazardous Materials, [online] 183(1-3), pp.565-573.

## Slide 9: Resilience - Final Equation Form

## Slide 10: Contribution and Cost Benefit Analysis Results
Contribution Weightings of Indicators of Resilient Design
Average weighting: 7.6
Range: 3-10
Cost-Benefit Ratings of Indicators of Resilient Design
Average weighting: 74
Range: 25-200

## Slide 11: Case Study Results
Case Studies:
1) Ammonia and Urea Facility – Houston, Texas
2) p-Aminophenol and Aniline Facility - Mumbai-Pune Industrial Area, India
Resilience Results of Case Study 1 and 2
 | Case Study 1 | Case Study 2
Indicators of Resilient Design | 2.28 × 1016 | 1.17 × 1016
Potential Impact | 7.22 × 108 | 2.63 × 109
Vulnerability | 2.26 × 108 | 4.87 × 108
Resilience, Ψ | 1.40 × 10-1 | 9.12 × 10-3

## Slide 12: Case Study Results
Conclusion after trials:
Safety analysis must be expanded to include specific resilience considerations
This model is appropriately sensitive to all factors of resilience
Resilience Results of Case Study 1 and 2
 | Case Study 1 | Case Study 2
Indicators of Resilient Design | 2.28 × 1016 | 1.17 × 1016
Potential Impact | 7.22 × 108 | 2.63 × 109
Vulnerability | 2.26 × 108 | 4.87 × 108
Resilience, Ψ | 1.40 × 10-1 | 9.12 × 10-3

## Slide 13: Improving Resilience
 | Design A | Design B
Indicators of Resilient Design | 5.83 × 1016 | 1.17 × 1016
Potential Impact | 2.63 × 109 | 2.76 × 108
Vulnerability | 4.87 × 108 | 4.87 × 108
Resilience, Ψ | 4.56 × 10-2 | 8.69 × 10-2
Case Study 2, Adjusted for Improved Resilience
Design A – improvements made via indicators of resilient design
Design B – improvements made via factors of potential impact and/or vulnerability

## Slide 14: Putting This Model to Use
Excellent Resilience
Unsatisfactory Resilience
Good Resilience
Develop a resilience database to contextualise model results

## Slide 15: And Finally
This model:
Presents resilience clearly for easy understanding
Is developed with the philosophy of accessibility and being straightforward to complete
Has potential to become a standardised analysis used across process sectors
Thank you for watching