## Slide 1
Threshold Quantity for Process Safety Metrics for Special / Coded Chemicals
By
Hema Divya Katna – khdivya@gmail.com
Rahul Raman – rahul@kaypear.com

## Slide 2
Essential element in improving the process safety program is to identify existing process safety performance to improve future performance
To improve the performance, a company has to implement leading and lagging process safety metrics
Lagging indicators measures what has already happened, such as accidents and injuries
Lagging process metrics can be developed using the following guideline document CCPS Process Safety Metrics and API-754 and HSG-254
Major step involved in implementation is grouping the compounds based on its physical and chemical properties to define its threshold quantities
Introduction

## Slide 3
Guideline - organization adopting this guidance already have sufficient safety management systems, the emphasis is on ensuring that their risk controls are effective and functioning as intended.
The lagging and leading process safety indicators are identified based on the hazards involved.
  Step 1 - formation of the team and allotting their roles and responsibilities.
  Step 2 - the scope, and hazard identification.
  Step 3 - identify the risk controls available, set them as lagging indicator.
  Step 4 - identify the critical elements of each risk control, set them as leading indicator.
  Step 5 - collect the data of the risk controls and have a reporting system.
  Step 6 - audit and review the data at frequent intervals.
HSG 254 – Process Safety Metrics

## Slide 4
Guidance provided is not exhaustive
Especially leaves interpretation of determining threshold quantities for chemical compounds with ambiguity due to the material complexities in a multi-product plant
Standards are US-centric and more guidance is needed for companies who want to implement it in a global scale
Difficulty faced by these companies are grouping the materials and assigning the correct threshold quantities
As these companies use coded chemicals and introduce at least 50 new compounds in 2-3 months of time frame
Problems Faced In Using Guideline

## Slide 5
Set Too High
Underreporting of Incidents
Delayed Response to Safety Issues
Inaccurate Lagging Indicators
Reduced Focus on Safety Improvement
Risk Accumulation
Safety Culture Impact
Regulatory Compliance
Why is assigning threshold quantities important
Set Too Low
Increased Reporting of Minor Incidents
Inflated Lagging Indicators
Resource Drain
Loss of Focus on Critical Issues
Diminished Employee Engagement
Risk of Data Manipulation
Misallocation of Resources

## Slide 6
Use UNDG Classification - primary method
Globally Harmonized System of Classification and Labelling of Chemicals - GHS Standard - primary method
Simple characteristics such as toxicity, flammability or corrosivity of the compound - OR statement classification - secondary method
Understanding the Classification – Based on CCPS and API-754
Threshold Quantities of a compound
OR Statement Classification
United NationsDangerous Goods Packing Group, UNDGL
Globally Harmonized System of Classification and Labelling of Chemicals, GHS

## Slide 7
UNDG classification and secondary method of classification
One compound can be classified in more than one class by the supplier based on transportation rules
OR statement classification a compound can have two characteristics at the same time
Example - styrene is reactive, toxic, and flammable
Precedence table based on the Department Of Transportation (DOT) regulations - used to determine which property or class/packing group of the compound to be used to determine the threshold quantities
Precedence of Hazard Characteristics

## Slide 8
Threshold Quantities for Toxic Vapours
Based on Toxicity – Gases
Zones | Inhalation Toxicity | Threshold Quantities for Tier-1 (Outdoor) | Threshold Quantities for Tier-1 (Indoor) | Threshold Quantities for Tier-2 (Outdoor) | Threshold Quantities for Tier-2 (Indoor)
Hazard Zone A | LC50 less than or equal to 200 ppm | 5 kg (11 lb) | 0.5 kg (1.1 lb) | 0.5 kg (1.1 lb) | 0.25 kg (0.55 lb)
Hazard Zone B | LC50 greater than 200 ppm and less than or equal to 1000 ppm | 25 kg (55 lb) | 2.5 kg (5.5 lb) | 2.5 kg (5.5 lb) | 1.25 kg (2.75 lb)
Hazard Zone C | LC50 greater than 1000 ppm and less than or equal to 3000 ppm | 100 kg (220 lb) | 10 kg (22 lb) | 10 kg (22 lb) | 5 kg (11 lb)
Hazard Zone D | LC50 greater than 3000 ppm or less than or equal to 5000 ppm | 200 kg (440 lb) | 20 kg (44 lb) | 20 kg (44 lb) | 10 kg (22 lb)

## Slide 9: Based on Toxicity – Liquids
V is the saturated vapor concentration in air of the material in mL/m3 at 20 °C and standard atmospheric pressure.
Volatility Vi is given by
Where, Pi is vapor pressure in kPa at 20 °C and standard atmospheric pressure.
Zones | Vapor concentration and toxicity | Threshold Quantities for Tier-1 (Outdoor) | Threshold Quantities for Tier-1 (Indoor) | Threshold Quantities for Tier-2 (Outdoor) | Threshold Quantities for Tier-2 (Indoor)
Hazard Zone A | V ≥ 500 LC50 and LC50 ≤ 200 mL/m3 | 5 kg (11 lb) | 0.5 kg (1.1 lb) | 0.5 kg (1.1 lb) | 0.25 kg (0.55 lb)
Hazard Zone B | V ≥ 10 LC50; LC50 ≤ 1000 mL/m3; and the criteria for Packing Group I, Hazard Zone A are not met. | 25 kg (55 lb) | 2.5 kg (5.5 lb) | 2.5 kg (5.5 lb) | 1.25 kg (2.75 lb)
Packing Group II | V ≥ LC50; LC50 ≤ 3000 mL/m3; and the criteria for Packing Group I, are not met. | 1000 kg (2200 lb) | 100 kg (220 lb) | 100 kg (220 lb) | 50 kg (110 lb)
Packing Group III | V ≥ 0.2LC50; LC50 ≤ 5000 mL/m3; and the criteria for Packing Group I and II, are not met. | 2000 kg (4400 lb) | 200 kg (440 lb) | 200 kg (440 lb) | 100 kg (220 lb)

## Slide 10: Based on Oral, Dermal and Inhalation of mists and dusts
Threshold Quantities for Oral, Dermal and Inhalation mists and dusts
Oral Toxicity LD50 (mg/kg) | Dermal Toxicity LD50 (mg/kg) | Inhalation mists and dusts LC50 (mg/L) | Threshold Quantities for Tier-1 (Outdoor) | Threshold Quantities for Tier-1 (Indoor) | Threshold Quantities for Tier-2 (Outdoor) | Threshold Quantities for Tier-2 (Indoor)
Less than equal to 5 | Less than equal to 50 | Less than equal 0.2 | 500 kg (1100 lb) | 50 kg (110 lb) | 50 kg (110 lb) | 25 kg (55 lb)
Greater than 5 and less than equal to 50 | Greater than 50 and less than equal to 200 | Greater than 0.2 and less than equal to 2 | 1000 kg (2200 lb) | 100 kg (220 lb) | 100 kg (220 lb) | 50 kg (110 lb)
Greater than 50 and less than equal to 300 | Greater than 200 and less than equal to 1000 | Greater than 2 and less than equal to 4 | 2000 kg (4400 lb) | 200 kg (440 lb) | 200 kg (440 lb) | 100 kg (220 lb)

## Slide 11: Based on Flammability
Threshold Quantities for flammability
Description | Threshold Quantities for Tier-1 (Outdoor) | Threshold Quantities for Tier-1 (Indoor) | Threshold Quantities for Tier-2 (Outdoor) | Threshold Quantities for Tier-2 (Indoor)
Flammable gases | 500 kg (1100 lb) | 50 kg (110 lb) | 50 kg (110 lb) | 25 kg (55 lb)
Liquids with normal boiling point less than 35 °C (95 °F) and flash point less than 23 °C (73 °F) |  |  |  | 
Liquids with normal boiling point greater than 35 °C (95 °F) and flash point less than 23 °C (73 °F) | 1000 kg (2200 lb) | 100 kg (220 lb) | 100 kg (220 lb) | 50 kg (110 lb)
Liquids with flash point greater than equal to 23 °C (73 °F) and less than and equal to 60 °C (140 °F) | 2000 kg (4400 lb) | 200 kg (440 lb) | 200 kg (440 lb) | 100 kg (220 lb)
Liquids with flash point greater than 60 °C (140 °F) released at a temperature at or above flash point |  |  |  | 
Liquids with flash point greater than 60 °C (140 °F) and less than equal to 93 °C (200 °F) released at a temperature below flash point | N/A | N/A | 1000 kg (2200 lb) | 500 kg (1100 lb)

## Slide 12: Based on Crude Oil
Threshold Quantities for Crude Oil
Description | Threshold Quantities for Tier-1 (Outdoor) | Threshold Quantities for Tier-1 (Indoor) | Threshold Quantities for Tier-2 (Outdoor) | Threshold Quantities for Tier-2 (Indoor)
Crude oil less than equal to 15 API Gravity (unless actual flash point available) | 1000 kg (2200 lb) | 100 kg (220 lb) | 100 kg (220 lb) | 50 kg (110 lb)
Crude oil greater than 15 API Gravity (unless actual flash point available) | 2000 kg (4400 lb) | 200 kg (440 lb) | 200 kg (440 lb) | 100 kg (220 lb)

## Slide 13: Based on Corrosivity
Threshold Quantities for Corrosivity
Description | Threshold Quantities for Tier-1 (Outdoor) | Threshold Quantities for Tier-1 (Indoor) | Threshold Quantities for Tier-2 (Outdoor) | Threshold Quantities for Tier-2 (Indoor)
Strong acids/bases, (substances with GHS Skin Corrosion Category 1A (exposure less than equal to 3 minutes during an observation period less than equal than 1 hour) or substances with pH less than 1 or pH greater than 12.5 | N/A | N/A | 1000 kg (2200 lb) | 500 kg (1100 lb)

## Slide 14: Flowchart for OR Statement Classification
Check the flash point and boiling point
No
Use toxic vapor classification based on Section 3.11 and Table-1
Gas
Start
Open the safety data sheet (SDS)
Is LC50 inhalation toxicity vapours less than 5000 ppm?
Yes
Check physical state of the compound
Liquid
Use toxic liquid classification based on Section 3.1.2 and Table 2
Use flammability classification based on Section 3.2 and Table -4
If the values are between Table-4
Use crude oil classification based on Table - 5
Crude Oil
Use classification based on Table-3
Yes
No
If skin corrosion category 1A or substances with pH less than 1 or pH greater than 12.5
Use classification based on Table - 6
Yes
No classification, use conservative approach.
No
If multiple classification applied, use worst scenario (lowest Threshold Quantities) or Determine the packing group use precedence table from DOT [6]
Multiple
Check oral, dermal or inhalation dusts and mists
No

## Slide 15: Example for OR Statement Usage
Styrene
Source of MSDS: fishersci [9]
Step -1: Check the toxic LC50 Inhalation
LC50 = 11.7 mg/L
LC50 = 2746.66 ppm
We should use toxic liquid as the physical state is liquid
Pi = 7 mbar = 0.7 kPa
Vi > LC50, LC50 < 3000
So,
Tier I (Outdoor) = 1000 kg (2200 lb)
Tier I (Indoor) = 100 kg (220 lb)
Tier II (Outdoor) = 100 kg (220 lb)
Tier II (Indoor) = 50 kg (110 lb)
Methanol
Source: Pioneer Forensics [10]
Step -1: Check the toxic LC50 Inhalation
LC50 = 81778.67 ppm for 4 hrs
LC50 > 5000 ppm
Step-2: Check the boiling point and flash point
Boiling point = 64.7 °C
Flash point = 12 °C
Using flammability classification
Tier I (Outdoor) = 1000 kg (2200 lb)
Tier I (Indoor) = 100 kg (220 lb)
Tier II (Outdoor) = 100 kg (220 lb)
Tier II (Indoor) = 50 kg (110 lb)
    Sodium Hydroxide
Source of MSDS: DCM Shriram [11]
Step -1: Check the toxic LC50 Inhalation
LC50 = Not available
Step-2: Check the boiling point and flash point
Boiling point = Not available
Flash point = Not available
Step-3: Check the oral, dermal and inhalation dusts and mists
Oral, dermal and inhalation dusts and mists = Not available
Step-4: Check pH and skin corrosivity category
pH = 13 to 14
Using corrosivity classification
Tier I (Outdoor) = NA
Tier I (Indoor) = NA
Tier II (Outdoor) = 1000 kg (2200 lb)
Tier II (Indoor) = 500 kg (1100 lb)

## Slide 16: Flowchart for UNDG Classification
Open the safety data sheet (SDS)
Start
Check if compound there in UNDGL
Use packing group, from the UNDGL
Yes
Check the packing group from safety data sheet
No
Use packing group, to determine the Threshold Quantities
Yes
No
Check the UNDG Code from the SDS and cross reference it with the UNDGL List
Use packing group, to determine the Threshold Quantities
Yes
No
Check the class of the compound
Determine the packing group from UNDG, use precedence table from DOT [6] or use worst scenario (lowest Threshold Quantities)
Multiple
Yes
Use class and determine the packing group from UNDGL
Use conservative approach
No

## Slide 17: Example for UNDG Classification
Styrene
Step -1: Check if the compound there in UNDGL
It is classified in Class 3, Packing Group III
So,
Tier I (Outdoor) = 2000 kg (4400 lb)
Tier I (Indoor) = 200 kg (440 lb)
Tier II (Outdoor) = 200 kg (440 lb)
Tier II (Indoor) = 100 kg (220 lb)
Let us assume, it is not there in UNDGL [4] list
Step-2: Check in SDS
Source of MSDS: fishersci [9]
Classified in Packing Group III
So,
Tier I (Outdoor) = 2000 kg (4400 lb)
Tier I (Indoor) = 200 kg (440 lb)
Tier II (Outdoor) = 200 kg (440 lb)
Tier II (Indoor) = 100 kg (220 lb)
Methanol
Source: Pioneer Forensics [10]
Step -1: Check if the compound there in UNDGL
It is classified in Packing Group II
So,
Tier I (Outdoor) = 1000 kg (2200 lb)
Tier I (Indoor) = 100 kg (220 lb)
Tier II (Outdoor) = 100 kg (220 lb)
Tier II (Indoor) = 50 kg (110 lb)
Let us assume, it is not there in UNDGL [4] list
Step-2: Check in SDS
Source of MSDS: Sigma Aldrich [12]
Classified in Packing Group II
So,
Tier I (Outdoor) = 1000 kg (2200 lb)
Tier I (Indoor) = 100 kg (220 lb)
Tier II (Outdoor) = 100 kg (220 lb)
Tier II (Indoor) = 50 kg (110 lb)
Let us assume, the packing group is not there in the SDS as well
Step-3: Check the class the compound
Source of MSDS: Sigma Aldrich [12]
Class of methanol 3, packing group II and 6.1 packing group II
Based on Precedence Table [6], Class 3 Packing Group II is preferred
So,
Tier I (Outdoor) = 1000 kg (2200 lb)
Tier I (Indoor) = 100 kg (220 lb)
Tier II (Outdoor) = 100 kg (220 lb)
Tier II (Indoor) = 50 kg (110 lb)

## Slide 18: Example for UNDG Classification
Sodium Hydroxide
Step -1: Check if the compound there in UNDGL
In this case, refer to the physical properties if solid or vapor and then decide the packing group. Here let us assume its solid
It is classified has packing group II
So,
Tier I (Outdoor) = 1000 kg (2200 lb)
Tier I (Indoor) = 100 kg (220 lb)
Tier II (Outdoor) = 100 kg (220 lb)
Tier II (Indoor) = 50 kg (110 lb)

## Slide 19: Flowchart for GHS Classification
Use statements to determine Threshold Quantities
Yes
Start
Open the safety data sheet
Check the hazard statements
If multiple classification applied, use worst scenario (lowest Threshold Quantities)
Multiple
No
Use conservative approach

## Slide 20: Example for GHS
Styrene
Source of MSDS: eChem Portal [13]
The hazard statements are
H226 – Flammable Liquid Category 3
H315 – Skin Irritation Category 2
H319 - Eye Irritation Category 2
H332 - Acute Toxicity Category 4
Based on the hazard statements H332 - Acute Toxicity Category 4, is having the lowest threshold quantities
So,
Tier I (Outdoor) = 200 kg (440 lb)
Tier I (Indoor) = 20 kg (44 lb)
Tier II (Outdoor) = 20 kg (44 lb)
Tier II (Indoor) = 10 kg (22 lb)
Methanol
Source of MSDS: eChem Portal [14]
The hazard statements are
H225 – Flammable Liquid Category 2
H301 – Acute Toxicity Category 3
H311 - Acute Toxicity Category 3
H331 - Acute Toxicity Category 3
Based on the hazard statements H331 - Acute Toxicity Category 3, is having the lowest threshold quantities
So,
Tier I (Outdoor) = 100 kg (220 lb)
Tier I (Indoor) = 10 kg (22 lb)
Tier II (Outdoor) = 10 kg (22 lb)
Tier II (Indoor) = 5 kg (11 lb)
    Sodium Hydroxide
Source of MSDS: eChem Portal [15]
The hazard statements are
H314 – Skin Corrosion Category 1A
H319 – Eye Irritation Category 2
H315 – Skin Irritation Category 2
Based on the hazard statements H314 - Skin Corrosion Category 1A, is having the lowest threshold quantities
So,
Tier I (Outdoor) = NA
Tier I (Indoor) = NA
Tier II (Outdoor) = 1000 kg (2200 lb)
Tier II (Indoor) = 500 kg (1100 lb)

## Slide 21: Conclusion
Compounds | OR Statement | United Nations Dangerous Goods Packing Group, UNDGL | GHS Method
Styrene | Tier I (Outdoor) = 1000 kg (2200 lb) | Tier I (Outdoor) = 2000 kg (4400 lb) | Tier I (Outdoor) = 200 kg (440 lb)
 | Tier I (Indoor) = 100 kg (220 lb) | Tier I (Indoor) = 200 kg (440 lb) | Tier I (Indoor) = 20 kg (44 lb)
 | Tier II (Outdoor) = 100 kg (220 lb) | Tier II (Outdoor) = 200 kg (440 lb) | Tier II (Outdoor) = 20 kg (44 lb)
 | Tier II (Indoor) = 50 kg (110 lb) | Tier II (Indoor) = 100 kg (220 lb) | Tier II (Indoor) = 10 kg (22 lb)
 |  | Assumption 1 – Based on the MSDS | 
 |  | Tier I (Outdoor) = 2000 kg (4400 lb) | 
 |  | Tier I (Indoor) = 200 kg (440 lb) | 
 |  | Tier II (Outdoor) = 200 kg (440 lb) | 
 |  | Tier II (Indoor) = 100 kg (220 lb) | 
Methanol | Tier I (Outdoor) = 1000 kg (2200 lb) | Tier I (Outdoor) = 1000 kg (2200 lb) | Tier I (Outdoor) = 100 kg (220 lb)
 | Tier I (Indoor) = 100 kg (220 lb) | Tier I (Indoor) = 100 kg (220 lb) | Tier I (Indoor) = 10 kg (22 lb)
 | Tier II (Outdoor) = 100 kg (220 lb) | Tier II (Outdoor) = 100 kg (220 lb) | Tier II (Outdoor) = 10 kg (22 lb)
 | Tier II (Indoor) = 50 kg (110 lb) | Tier II (Indoor) = 50 kg (110 lb) | Tier II (Indoor) = 5 kg (11 lb)
 |  | Assumption 1 – Based on the MSDS | 
 |  | Tier I (Outdoor) = 1000 kg (2200 lb) | 
 |  | Tier I (Indoor) = 100 kg (220 lb) | 
 |  | Tier II (Outdoor) = 100 kg (220 lb) | 
 |  | Tier II (Indoor) = 50 kg (110 lb) | 
 |  | Assumption 2 - Based on the class | 
 |  | Tier I (Outdoor) = 1000 kg (2200 lb) | 
 |  | Tier I (Indoor) = 100 kg (220 lb) | 
 |  | Tier II (Outdoor) = 100 kg (220 lb) | 
 |  | Tier II (Indoor) = 50 kg (110 lb) | 
Sodium Hydroxide | Tier I (Outdoor) = NA | Tier I (Outdoor) = 1000 kg (2200 lb) | Tier I (Outdoor) = NA
 | Tier I (Indoor) = NA | Tier I (Indoor) = 100 kg (220 lb) | Tier I (Indoor) = NA
 | Tier II (Outdoor) = 1000 kg (2200 lb) | Tier II (Outdoor) = 100 kg (220 lb) | Tier II (Outdoor) = 1000 kg (2200 lb)
 | Tier II (Indoor) = 500 kg (1100 lb) | Tier II (Indoor) = 50 kg (110 lb) | Tier II (Indoor) = 500 kg (1100 lb)

## Slide 22: Conclusion
Based on the three approaches, a company has to use a consistent approach for all the compounds.
Choosing the Safety Data Sheet (SDS) is the key factor, company should use an appropriate safety data sheet during the process of classification.
Company has to decide a conversative approach for the classification.
Above table shows that different Threshold Quantities can be obtained when using the various approaches.
The GHS classification is most conservative due to the lower threshold values.
Companies dealing with many coded/special chemicals with global operations must determine the best classification method and consistent so that they can obtain proper process safety metrics across various sites.

## Slide 23: Thank You
You can’t improve what you don’t measure – Peter Drucker