## Slide 1: Safety Critical Task Analysis Practical Examples and Application
Toby Garner BSc, MSc, C.ErgHF
Human Factors Consultant
Monaco Engineering Solutions

## Slide 2: Application of SCTA
Fig.1 – SCTA Process Overview
SCTA input to:
Design decisions
Risk-based procedure development
Operational concept definition
Performance standards
Resilience planning
Safety Case
Assurance activities
Continuous improvement

## Slide 3: Worldwide application of SCTA
Application of SCTA is global.
The SCTA method applied across different safety critical industries.
Includes also coaching SCTA to site & human performance staff.
Fig.1 – Application of SCTA

## Slide 4: SCTA Examples
Vessel Design (maritime) - Korea
1
2
Guidance: Vessel Deck Design:
Mooring Equipment Guidelines (MEG4, OCIMF), 2018.
3
Incident Investigation (offshore) – N. Europe
Safety Case (COMAH site) - UK
Guidance: SCTA Guidance, Energy Institute (EI), 2020.
Guidance: IOGP (2018), TopSet, Energy Institute (2020), NOPSEMA

## Slide 5
Vessel Design (maritime)
1
Guidance: Vessel Deck Design:
Mooring Equipment Guidelines (MEG4, OCIMF), 2018. Section 2.
SCTA Aim
Design for safe maintenance / operation (LNG Carrier)
Fig.1 – Typical mooring arrangement
Fig.2 – Design plans
Falling from height
Crew overboard / Falling into the water
Hit by flying objects (e.g., snapback)
Entanglement, entrapment, or crush injuries
Vessel damage
Product Release
Mooring Hazards include
Example 1 - Liquefied Natural Gas (LNG) Carrier Vessel Design

## Slide 6
Vessel Design (maritime)
1
Guidance: Vessel Deck Design:
Mooring Equipment Guidelines (MEG4, OCIMF), 2018. Section 2.
Fig. 3 - MEG4 SCTA process
Fig.1 – Typical mooring arrangement
Fig.2 – Design plans
SCTA process
Task scenarios include:
  Pier / Jetty
  Ship-to-ship mooring (FSRU)
  Emergency tugboat
  Canal transit
  Bunkering / Loading
Example 1 - Liquefied Natural Gas (LNG) Carrier Vessel Design

## Slide 7
Human Errors
Example 1 - Liquefied Natural Gas (LNG) Carrier Vessel Design
Performance Shaping factors
Notes: Performance Shaping Factors Include:
  Command’s situational awareness of mooring team
  Crew risk awareness
  Physically demanding / fatigue
  Suboptimal environment conditions

## Slide 8
Remote winch operations
Clear sightlines over mooring
Guardrail / barrier protection
CCTV coverage
Snap-back area warning
Safe locations for mooring team
Lighting coverage
Reduction in obstructions
Line tension monitoring systems
SCTA Recommendations
Identification of Safety critical task
Further consideration
Existing Safeguard
Example 1 - Liquefied Natural Gas (LNG) Carrier Vessel Design

## Slide 9
2
Safety Case (COMAH)
Guidance: SCTA Guidance, Energy Institute (EI), 2020.
Fig.2 – Major Accident Hazards
Fig.1 – LPG distribution site
Example 2 – COMAH Safety Case

## Slide 10
2
Safety Case (COMAH)
Guidance: SCTA Guidance, Energy Institute (EI), 2020.
Fig.1– SCTA excerpt
Fig.1 – Tanker offloading
Example 2 – COMAH Safety Case

## Slide 11
2
Safety Case (COMAH)
Guidance: SCTA Guidance, Energy Institute (EI), 2020.
Fig.1 – Tanker offloading
Fig.2 – Example Recommendations
Example 2 – COMAH Safety Case

## Slide 12: Example 3 - Deck Cadet fatality
3
Incident Investigation (offshore)
Guidance: IOGP (2018), TopSet, Energy Institute (2020), NOPSEMA
SCTA Aim
Derive Human Factors learnings from a fatal accident.
Accident Overview
Deck Cadet fell from height (8m).
Fell through open grating that was being cleaned.
Initial conclusion ‘Cadet at fault from entering unsafe area’
i.e., human error.
Fig.2 - Accident report form
Fig. 1 – Incident Overview

## Slide 13: Example 3 - Deck Cadet fatality
Fig.1 - Timeline with actors/critical events

## Slide 14: Example 3 - Deck Cadet fatality
Fig.1 - Performance Shaping Factors

## Slide 15: SCTA Learnings
Relies upon participation and contribution of various disciplines e.g., workshops, site walk-throughs (if possible).
The method should be proportionately applied (e.g., error types, number of safety critical tasks, type of safeguards).
Value of SCTA is from challenging the way people think about safety and human error.
It is an opportunity to generate, record and integrate improvement ideas from staff members into a company’s management process.

## Slide 16
Mr Toby Garner (MES Human Factors Consultant)
toby.garner@mes-international.com