## Slide 1: Bioprocessing 4.0: Minimising Cost of mRNA Vaccine Manufacturing
Kesler Isoko a,b, Mahdi Ahmed b, Joseph Middleton b, Joan L. Cordiner b, Zoltan Kis b,c*, Peyman Z. Moghadam a*
a Department of Chemical Engineering, University College London, Torrington Place, London WC1E 7JE, United Kingdom
b School of Chemical, Materials and Biological Engineering, University of Sheffield, Mappin Street, Sheffield S1 3JD, UK
c Department of Chemical Engineering, Imperial College London, South Kensington Campus, London SW7 2AZ, UK
uceckis@ucl.ac.uk

## Slide 2: The Goal: Recycling Expensive Raw Materials
Opportunity
Recycling expensive reagents could significantly reduce the cost of mRNA (2-5x)
Problem
However, this process is still very manual, and the high dead-times, low observability make it challenging to control
(Nair et.al., 2025 ~ draft; patent - PCTGB2024/052819) ~ filed

## Slide 3: Control Setup in mRNA Recycling
Variable Names | Notation | Example
Prediction Horizon | P | Number of steps the model predicts
Control Horizon | M | Number of control actions evaluated
Control Outputs | Y | RNA yield
Reference Trajectory | r | Desired Yield Response
State Variables | x | Other Components i.e. DNA Template
Control Inputs | U | NTPs Valve Position
Measurements
pH can be used to monitor the reaction
Objective
Our goal is to feed NTP such that we maximise yield with minimum side-effects such as pyrophosphate ions production

## Slide 4: Control Setup: Dynamic Model
Variable Names | Notation | Example
Prediction Horizon | P | Number of steps the model predicts
Control Horizon | M | Number of control actions evaluated
Control Outputs | Y | RNA yield
Reference Trajectory | r | Desired Yield Response
State Variables | x | Other Components i.e. DNA Template
Control Inputs | U | NTPs Valve Position
Measurements
pH can be used to monitor the reaction
Objective
Our goal is to feed NTP such that we maximise yield with minimum side-effects such as pyrophosphate ions production

## Slide 5: Dynamic model development: Data Driven
Purely data-driven (System identification)
AutoRegressive with eXogenous inputs (ARX)
Nonlinear AutoRegressive with eXogenous inputs (NARX)
Neural Networks (RNN, LSTMs, etc…)
Purely Mechanistic (with state estimation)
Extended Kalman Filters (EKF), Unscented Kalman Filters (UKF), Kalman Filters (KF)
Process Analytical Technologies (PAT)
Soft sensors
Hybrid semi-parametric modelling
Serial
Parallel
Pros of data-driven
No first principal knowledge required
Linear models generates a quadratic optimisation programme (convex) that can be solved reliably online
Cons of data-driven
ARX Might not capture nonlinear dynamics leading to instability
Requires enough step response data or access to plant to calibrate dead-time, rise-time and steady states parameters

## Slide 6: Control Setup: Dynamic Model
Variable Names | Notation | Example
Prediction Horizon | P | Number of steps the model predicts
Control Horizon | M | Number of control actions evaluated
Control Outputs | Y | RNA yield
Reference Trajectory | r | Desired Yield Response
State Variables | x | Other Components i.e. DNA Template
Control Inputs | U | NTPs Valve Position
Measurements
pH can be used to monitor the reaction
Objective
Our goal is to feed NTP such that we maximise yield with minimum side-effects such as pyrophosphate ions production

## Slide 7
Purely mechanistic
Moving Horizon Estimation
PAT
Soft sensor for key variables
Methodology
Dynamic model development: Mechanistic
Linearisation techniques lead to poor performance (EKF)
UKF is accurate however requires proper calibration and is too slow to be integrated in optimisation loop

## Slide 8: Developing a PAT sensor
Pros
Provides accurate estimates of NTP & RNA
Cons
Numerical instability of the log in python due to floating point errors
Sensitive to noisy measurements

## Slide 9: Soft sensor development: Physics-informed Gaussian Process Regression
Requirements
Keep the physics
Sampling efficient
Robust to noisy measurements
Gaussian Processes
Follow a Bayesian formulation
Require little data
Uncertainty Quantification

## Slide 10: Soft sensor development: Physics-informed Gaussian Process Regression
Two models deployment (complicated setup)
Error can carry over leading to unnecessary instability
Kinetic model performance was unsatisfactory

## Slide 11: Control Setup: Hybrid Model
Variable Names | Notation | Example
Prediction Horizon | P | Number of steps the model predicts
Control Horizon | M | Number of control actions evaluated
Control Outputs | Y | RNA yield
Reference Trajectory | r | Desired Yield Response
State Variables | x | Other Components i.e. DNA Template
Control Inputs | U | NTPs Valve Position
Measurements
pH can be used to monitor the reaction
Objective
Our goal is to feed NTP such that we maximise yield with minimum side-effects such as pyrophosphate ions production

## Slide 12
Hybrid semi-parametric model
Serial structure (ensemble)
Parallel structure (discrepancy, hierarchical)
Methodology
Dynamic model development: Hybrid Model
Evaluated ALL the relevant ML techniques
Support Vector Regression
Bayesian Regression
Gaussian Processes
Xgboost, Random Forest, LightGBM
Linear Regression, ElasticNet
Partial Least Squares
Levenberg-Marquardt (LMM) algorithm

## Slide 13: Control Setup: Optimiser
Variable Names | Notation | Example
Prediction Horizon | P | Number of steps the model predicts
Control Horizon | M | Number of control actions evaluated
Control Outputs | Y | RNA yield
Reference Trajectory | r | Desired Yield Response
State Variables | x | Other Components i.e. DNA Template
Control Inputs | U | NTPs Valve Position
Measurements
pH can be used to monitor the reaction
Objective
Our goal is to feed NTP such that we maximise yield with minimum side-effects such as pyrophosphate ions production

## Slide 14
Metrics
Colour – Steady state performance
Size – Control Effort
Factors
– control delta – Significant impact
– reference trajectory – No impact on performance
– control magnitude – Significant impact
Note
Reference trajectory range was not physically meaningful therefore, we will need to adopt economic MPC
MPC Controller Design: Tuning Parameters

## Slide 15
Methodology
– control delta
– reference trajectory
– control magnitude
MPC Controller Design: Control Effort

## Slide 16: Control Setup: Connectivity
Variable Names | Notation | Example
Prediction Horizon | P | Number of steps the model predicts
Control Horizon | M | Number of control actions evaluated
Control Outputs | Y | RNA yield
Reference Trajectory | r | Desired Yield Response
State Variables | x | Other Components i.e. DNA Template
Control Inputs | U | NTPs Valve Position
Measurements
pH can be used to monitor the reaction
Objective
Our goal is to feed NTP such that we maximise yield with minimum side-effects such as pyrophosphate ions production

## Slide 17
Methodology
OPC – for interoperability
MQTT – for lightweight robust communication
Industrial IoT Platform: Model Deployment and Connectivity

## Slide 18
Test Type I errors (False Positives)
Step 1: Increase Mg2+ flowrate to 1.25 L/min. (SAFE)
Step 2: Check new RNA yield prediction (≈7 g/L) within acceptance ranges so reaction continues.
Test Type II errors (False Negative)
Step 3: Increase Mg2+ flowrate to 2.00 L/min. (PRECIPITATION)
Step 4: Check new RNA yield prediction (≈5 g/L) outside acceptance ranges.
Step 5: The model shuts down the reaction (Set minimum flowrate to 50 𝜇L/min to prevent bad batch)
IIoT Platform Test Feedback

## Slide 19: IIoT Platform Soft Sensor Deployment

## Slide 20: Results
Hybrid model
accuracy: 85% in forecasting RNA yield
Soft sensor
  accuracy: 90% in estimating current NTPs & RNA concentrations
IIoT Platform Features:
  model deployment
  two-way data connectivity
  real-time visualisation
  MPC Controller
  Reduce Costs by 31% vs recycling w PID (85% vs Traditional)

## Slide 21: Results Hybrid Model vs Mechanistic Model
Hybrid model predictions on unseen data
Mechanistic model predictions on unseen data

## Slide 22
Results: soft sensor
Ceiling constrained successfully!
Non-linear relationship between pH and NTPs

## Slide 23
Plant simulation captures oscillatory dynamics in experimental data
Quantitative evaluation of the plant required
Results: Plant Simulator
MPC Response Profile
Regular Top-up Response Profile

## Slide 24
Model Predictive Controller minimises impurity (PPi)
MPC controller also maximises yield and maintains optimal operations
MPC controller achieves better stability and faster steady-state
Results: Multi-objective optimisation
MPC Response Profile
Regular Top-up Response Profile

## Slide 25
MPC makes use of manipulated variables (NTPs) much more effectively
This leads to higher yields of RNA using less reagent
Results: Multi-objective optimisation
$0.69
MPC costs $0.69 on the dollar compared to standard recycling
Compared to traditional (no recycling) is < 15% of the cost

## Slide 26: Summary & Future Work
Summary
Developed dynamic hybrid model and soft sensors for real-time predictions
Achieved multi-objective optimisation
Tested the control strategy in simulation demonstrating cost savings
Deployed dynamic model in predictive mode via a custom IIoT Platform
Future Work
Implement Economic MPC with GP-ARX model in the close-loop
Use Bayesian Optimisation to tune controller parameters
Deploy full-controller

## Slide 27: Acknowledgments Thanks for listening Any Questions?
Funding: Wellcome Leap R3 Programme, CEPI, H. Walter Stern Scholarship
Collaborators: Kesler Isoko, Mahdi Ahmed, Joseph Middleton, Joan L. Cordiner, Zoltan Kis, Peyman Z. Moghadam