## Slide 1
Trung Trinh, PhD
Research Scientist , SINTEF Industry, Norway
Roman Tschentscher, PhD
Senior Research Scientist , SINTEF Industry, Norway
Cloud-based Open-source Digital Twin for BioChemical Pilot Plant
Advances in the digitalisation of the process industries conference
Manchester, Oct 2025
Contact: trung.trinh@sintef.no

## Slide 2: Contents
Introduction to SINTEF
Digital Twin Concept for BioChemical Pilot Plant
Cloud Architecture
Machine Learning Models
Big Data Analytics & Visualization
Conclusion

## Slide 3
SINTEF
SINTEF
Digital
SINTEF Industry
SINTEF
Community
SINTEF Energy
SINTEF
Ocean
INSTITUTTER
SINTEF
AI
in
Domain
Norwegian Research Organization founded in 1950
Notes: SINTEF Manufacturing er ett av 6 institutter i forskningskonsernet SINTEF.
Vi er eid av:
SINTEF Holding AS 50,07%
Nammo Raufoss AS 14,43%
SIVA – Selskapet for industrivekst Sf 10,03%
Hydro Aluminium AS 6,07%
Benteler Aluminium Systems Norway AS 6,07%
Kongsberg Automotive AS 5,57%
Raufoss Technology AS 5,53%
Hexagon Composites ASA 2,23%
Eierstrukturen vår gjenspeiler våre røtter og bakgrunn.
Figur: SINTEF

## Slide 4: Digital Twin For Process Pilot
Cloud-based Automatic Control System
Sytem Control
Monitoring of Targets in Real-Time
Bigdata analytics for RD
Optimalization
Data Storage
ML Models
Process Unit
Pilot /Process
Data Platform on Azure VM
Pilot Managemet
Function 2
Function 3
Function 4
Function 5
Function 1
The Digital Twin:
AI, big data, autonomous systems, machine learning, and cloud solutions
The Digital Twin components:
Pilot
Data Platform
ML Models

## Slide 5: Tools for Digital Twins
  Kafka app: realtime stream data from Raman analysis equipment to data platform
  MQTT app: real-time communication between Cloud and control system of pilot
  PostgreSQL: TimescaleDB to collect realtime data from Raman and operation
  Python: Data processing linked to ML models
Machine learning models (PLSr, XGBoost, Baysiean Optimalization)
  Flask app: web app for visullization
  Grafana app: Real time monitoring
  Power BI app (Microsoft- license app): big data analytics
  Docker app: an environment for installing, running, and packaging all applications within a data platform.

## Slide 6: Cloud Architecture for The Digital Twins
ML Models
ML PLSr
ML XGBoost
Baysiean Optimalization
Realtime stream Raman spectra
Realtime stream Operation Conditions
Dashboard Big data Analytic and Offline Monitoring
Database
Database Modelling
(Star schema)
Azure VM
Realtime Monitoring
System Control
Web app for visullization
Reactor
Database
The end-to-end latency from sensors to the cloud dashboard,
including data processing and ML model execution,
is below 2 seconds.

## Slide 7: Cloud based Pilot System Control
Arduino
Raspberry Pi 4
Dashboard
Manual control
Auto-DOE control
Autonomous control
Pump 1
Pump 2
Flow meter 1
Sensor system
Camera
Reactor System
Design of Experiment (DOE)
Model
Flow meter 2
Database

## Slide 8: Machine Learning Models for The Digital Twin
Realtime Monitoring on cloud
ML Models
Web app for Enduser
ML Models
Raman analysis
Investigated conditions
Reactor
A highly valuable data resource containing 100 batches with 113935 dataset for all available process and Raman spectroscopy measurements from the University of Manchester and University College London
is used for model training and Big Data analytics in the digital twin platform.
1Modern day monitoring and control challenges outlined on an industrial-scale benchmark fermentation process, Computers and Chemical Engineering 130 (2019) 106471
Data Platform
Data Platform
Optimal Targets and Conditions

## Slide 9: Machine Learning Models for The Digital Twin
PLSr Model
Raman spectra treated by savfol-filter
  Used to convert Raman spectra into chemical concentrations
  The savgol_filter function in Python is used for smoothing data and eliminating background noise for model development
  2062 datasets applied (50% train - 50% test)
  Achieved R2: 0.997 - MSE calib: 0.228
1Modern day monitoring and control challenges outlined on an industrial-scale benchmark fermentation process, Computers and Chemical Engineering 130 (2019) 106471
Raman spectra (1)

## Slide 10: Machine Learning Models for The Digital Twin
XGBoost Model
  Predicts target concentrations based on operating conditions
  Trained on >100,000 datasets (1)
  80% train / 20% test - Cross validation
  Mean Squared Error Accuracy: 1.854
1Modern day monitoring and control challenges outlined on an industrial-scale benchmark fermentation process, Computers and Chemical Engineering 130 (2019) 106471

## Slide 11: Machine Learning Models for The Digital Twin
Bayesian Optimalization Model
New Features
Predicted Results
XGBoost Model
Optimal results
The Bayesian Optimization (BO) framework was initialized with 200 random points and further executed with 500 iterations to optimize the target.
👉 BO performed effectively after the initial 200 random points and showed significant improvement in the optimal values after ~400 iterations.
👉 Supports pilot optimization, reduces experimental costs, and enhances process efficiency

## Slide 12: Big Data Analytics for RD
113 935 datasets1 were processed and structured into a project–campaign–test hierarchy. The Power BI dashboard enables fast multi-level queries and real-time updates, supporting trend analysis and factor identification
The Power BI dashboard enables fast access to Big Data with multi-level relationships and is automatically updated from the database.
    👉 It supports the identification of target evolution trends and the factors influencing target performance
1Modern day monitoring and control challenges outlined on an industrial-scale benchmark fermentation process, Computers and Chemical Engineering 130 (2019) 106471

## Slide 13: Conclusion
SINTEF has successfully developed a digital twin platform
  based on open-source technologies and deployed on Azure Cloud VM.
  The system integrates ML models, data processing pipelines, and a time-series database, operating effectively for both real-time and batch processing.
The integrated Big Data analytics and optimization models provide strong support for
  accelerating research
  enabling faster and more accurate decision-making.