## Slide 1: UAO & IEC 61499 Advancing open Automation
Sarat Kumar Reddy Molakaseema
Chef Architect Officer
UniversalAutomation.org
Notes: Hi and welcome to this presentation about UniversalAutomation.Org.
My name is xxx and I am xxx

## Slide 2: Opening Message: Power with Purpose
WITH GREAT POWER COMES GREAT RESPONSIBILITY.
Use the power of AI wisely—
understand its opportunities and challenges in depth,
and act with responsibility and foresight.

## Slide 3: ASSET-BASED and ASSET-CENTRIC Industrial Automation
Introduction to Tterminology

## Slide 4: What is an ASSET?
A physically or logically identifiable entity that contributes to the operation, monitoring, or control
of an industrial system
Physical Assets:
Machines (e.g., CNC machines, robots)
Devices (e.g., sensors, actuators, PLCs)
Infrastructure (e.g., conveyors, tanks, valves)
Logical (Virtual) Assets:
Software modules (e.g., control logic, analytics)
Digital twins
Data models or services (e.g., OPC UA nodes, REST APIs)
Simple Asset
COMPOSITE ASSET
Simple Asset
Simple Asset
Simple Asset

## Slide 5: Asset Characterization
Asset
Identifiable – with a unique ID or name
Described – with metadata, manufacturer, capabilities…
Operable – Can be monitored and controlled
Composable – Can be integrated into larger system

## Slide 6: What is an Asset Facet?
An Asset Facet is a logical partition of an asset that refers to a specific perspective or aspect of an asset, that is of an interest to an actor interacting with the asset.
An Asset Facet is a specific view of an asset that highlights information or functionality relevant to a particular actor interacting with it.
Actor | Interacts With Facet(s) | Purpose
Operator | Control and Monitoring | Start/stop machines, view status, respond to alarms
Maintenance Technician | Diagnostics, Lifecycle, Configuration | Troubleshoot issues, perform maintenance
System Integrator | Communication, Configuration, Control | Set up network, configure parameters, deploy logic
Production Manager | Monitoring, Performance, Lifecycle | Monitor KPIs, plan maintenance, optimize throughput
Security Administrator | Security | Manage access rights, audit logs
Simulation | Digital Twin, Monitoring, Control | Simulate behavior, validate control logic
MES/ERP Systems | Identification, Lifecycle, Performance | Track asset usage, integrate with business processes

## Slide 7: Asset-BASED vs Asset-CENTRIC control
Asset-BASED control is the strategic development of control applications that ensure reliable plant or process operations by actively monitoring and managing assets. Its goal is to optimize asset performance, reliability, and lifespan - minimizing downtime, reducing maintenance costs, and extending operational life.
Examples:
Condition-based control of heat exchangers for energy efficiency.
Lifecycle-aware control of manufacturing robots to extend operational life.
Proactive control of pumps to avoid failures.
Asset-CENTRIC control is a strategic approach where control decisions are centered around the asset itself emphasizing operational ownership, lifecycle management, and value optimization by aligning control strategies with the asset’s performance, condition, and business objectives.
Example:
Scheduling heat exchanger operations and prioritizing maintenance based on business impact and return on investment (ROI), while applying condition-based control to optimize asset performance without compromising production goals.

## Slide 8: Asset-based vs Asset-centric control Continued…
Feature | Asset-Based Control Engineering | Asset-Centric Control
Focus | Control logic tied to asset condition | Control logic orchestration centered on asset value optimization and business objective.
Scope | Engineering and automation systems | Strategic orchetsration of control
Data to Use | Real-time sensor data for control | Lifecycle and performance data for planning and scheduling
Responsibility | Engineers and control system designers | Production and operations planning and scheduling business unit
Goal | Optimize control performance and asset reliability | Maximize asset value and operational efficiency ensuring business objectives and production goals are met

## Slide 9: Strategic control application Design & Development principles
Asset
Encapsulation
and
Abstraction
Modularity
and
Scalability
Decentralized and Distributed intelligence
Portability and Interoperability
Reusability and Configurability
Plug and
Produce
Software
Defined (Hardware Agnostic)
Vendor Independent (Openness)
Orchestration
Digital
integration and connectable

## Slide 10: Critical programming constructs
Object-based and Object-oriented programming
Service Oriented Architecture and Development
Event driven modelling and programming
State machines and state-based control & opeartion
Asynchronous communications